## Slide 1: Introduction of CCS and IRN system
Friday, June 7, 2024

## Slide 2: What is Autotoll?
Autotoll is a solution provider for IT industry.
Autotoll was established on 1 October 1998.
Office
  Billion Centre (Kowloon Bay), 2.5 floors, over 200 staff.
  Evergain Centre (Kwai Chung), over 20 staff.
  GZ E-Park, office 100 staff .

## Slide 3: What Autotoll is doing?
Current project
  Private sector
    CLP SOSS (Safely On-Site System), Entrance Control, Shutter Bus, Car booking
    Truck management (GPS), > 20 thousand vehicle monitored.
    RehaBus
    EV charging
    Jackson Coach
    OLTD for Skip
  Government sector
    eToll
    TD57/93 (stage 1, 2)
    Smart Lamp Post
    Land’s department, SPIMS (Smart Position Instrument Management System)
    Traffic Control System (Tunnel, highway), TMCA, CKR, TSCA…
    SCC (Smart City Consortium) Recycle Collection Project

## Slide 4: Background
Hong Kong Smart City Blueprint (https://www.smartcity.gov.hk/)
Six Major Areas:
Six Major Areas:
Smart mobility 智慧出行
(d) Intelligent Transport System and Traffic Management
智能運輸系統及交通管理
Smart living 智慧生活
Smart environment 智慧環境
Smart government 智慧政府
Smart economic 智慧經濟
Smart people 智慧市民
December 2017

## Slide 5: Background
One of the smart mobility initiatives is to install about 1200 traffic detectors on all strategic routes to provide real-time traffic information to the public via “HKeMobility” mobile app
The major project objective is to estimate average speeds on the strategic routes based on the segments of Intelligent Road Network (IRN) at 2-minute time interval.

## Slide 6: TD57/93 Data Flow Diagram

## Slide 7: TD57 – Total 454 AIDs

## Slide 8: TD57 – Total 70 BTs (171 BT pairs)

## Slide 9: TD57 – BlueARGUS (For BT only)

## Slide 10: TD57 – BlueARGUS (For BT only)

## Slide 11: TD93 – Total 367 AIDs

## Slide 12: TD93 – Total 263 BTs (638 BT pairs)

## Slide 13: TD93 – Trafficnow (DeepBlue) (For BT only)

## Slide 14: Major functions of CCS:

## Slide 15: 1. Locate AID/ BT/ Toll Point

## Slide 16: 2. Real time AID/BT data

## Slide 17: Toll point data

## Slide 18: 3. Real time traffic speed (HKeMobility)

## Slide 19: HKeMobility – Share same data source with CCS

## Slide 20: 4. Report

## Slide 21: Checking the latest or past data (speed) of IRN/BT/AID AID:

## Slide 22: Bluetooth:

## Slide 23: Road Segment (IRN)

## Slide 24: IRN (Intelligent Road Network)
Currently total 5693 IRNs on use (update continuously)
ꟷꟷꟷ Centerline
ꟷꟷꟷ IRN

## Slide 25: IRN calculation workflow

## Slide 26: IRN with AID Data
AID detectors:
Spot speed of individual vehicle & vehicle counts

## Slide 27: AID Data cleansing
Clean the spot speeds of individual vehicles collected by AID detector
- To eliminate unreasonable speeding data
The validated spot speed data of individual vehicles collected in every 2 minutes will then be used to calculate the average spot speed (i.e. time mean speed) in that 2-min time interval.
Example:
Speed limit = 80 km/h
Speed > (1+  %) of speed limit (say,  =10) will be screened out

## Slide 28: AID Data calibration (Time mean speed  space mean speed)
Calibrate the average spot speeds (i.e. time mean speed ) at 2-min interval based on the actual space mean speed vs by manual measurement -- from the video recodes of some AID detectors with typical detection zones
vs = 0.9554ut
R2 = 0.991
Differences between time mean speed (ut) and actual space mean speed (vs) from manual measurement
Standardized length of detection zones (say, 12m) is required to facilitate the calibration work for different sites
Calibration is based on the time mean speeds on the corresponding traffic lanes of the associated IRN segments
Space speed
Spot speed
12 m
12 m
12 m
IRN segment

## Slide 29: Data Fusion For Estimating Average Speeds on IRN Segments per Bound
Noted that AID detectors capture the spot speeds by traffic lane by direction. Thus, the space mean speeds will be calibrated based on the time mean speeds on the corresponding traffic lanes of the associated IRN segments.

## Slide 30: Data Fusion For Estimating Average Speeds on IRN Segments per Bound

## Slide 31: IRN with Bluetooth Data
Bluetooth (BT) detectors: Travel time between two BT detectors
MAC address: 00:11:22:33:FF:EE
10:32:00am
MAC address: 00:11:22:33:FF:EE
10:38:00am
Travel time between A and B = 6 min
A
B
Note that the measured travel time would be the actual travel time for the completed journey between two BT detectors.
Distance = 1.7 km
Measured travel time = 6 min
Average speed = 17 km/h

## Slide 32: Data Fusion for Estimating Average Speeds on IRN at 2-min Interval
Space mean speeds
at 2-min interval
(1) BT average travel time at 2-min interval
Estimated average speeds & times on IRN segments at 2-min interval
Calculate fusion ratio R
Resultant estimated average speeds on IRN segments at 2-min interval
Time mean speeds at 2-min interval (after data cleansing of AID spot speed data)
Linearization
Adjustment
Calibration
Space mean speed vs2
d1
d3
AID detector 2
AID detector 1
Space mean speed vs1
distance
d2

## Slide 33: Fusion Ratio
If fusion ratio R is too large or small
 R < 0.8 or R > 1.4, do not conduct data fusion due to inconsistency between BT and AID data
(1) Average travel time
(2) Average travel times over the time period taken

## Slide 34: Example
3 IRN segments are divided into 6 small segments
With AID data only
1.0 km
0.8 km
1.2 km
1
2
3
4
5
6
0.4 km
0.6 km
0.8 km
0.3 km
0.9 km
0.2 km
With AID data only
IRN segment 1
IRN segment 2
IRN segment 3
BT
AID
AID
AID
BT
Segments with both BT and AID data

## Slide 35: IRN Segments with AID Detector Data Only:
Estimate the Average Speed on IRN based on AID Speed Data Only
Use Speed Limit
No. of Validated AID Speed Data at 2-min Intervals > 0
No. of Validated AID Speed Data at 2-min Intervals = 0
(1)
(2)
BT
AID
AID
AID
BT
With AID data only
With AID data only

## Slide 36: IRN Segments with Both BT and AID Detector Data:
BT Travel Time Data at 2-min Interval
Fuse BT Travel Time and AID Speed Data by fusion ratio R* for Average Speed Estimation on IRN at 2-min Interval
No. of Validated AID Speed Data at 2-min Interval > 0
(3a)
Estimate the Average Speed on IRN based on AID Speed Data Only
No. of Validated AID Speed Data at 2-min Interval > 0
(3b)
BT Travel Time Data at 2-min Interval (but without change in 3 or more successive time intervals)
Segments with both BT and AID data
BT
AID
AID
AID
BT
* 0.8  R  1.4

## Slide 37: Malfunction of BT and/or AID Detectors
BT Detector | AID Detector | Estimation of Average Traffic Speeds on IRN Road Segments
 |  | Based on AID speed data only
 |  | Use the most updated relevant historical data
 |  | Use the most updated relevant historical data
Note:  = out of order without real-time data

## Slide 38: Scenario
AID07102 (In Tseung Kwan O) is blocked by the tree

## Slide 39: Solution
IRNs 7122-7127, 7290, 7308 originally AID07102~AID07103;
Are replaced by BT pair JTS0701~JTS0702

## Slide 40: Summary
AID Detectors
Bluetooth (BT) Detectors
AID Software
BT Software
Ingress Engine
Data Cleansing
Central Computer System (CCS)
Data Fusion for Estimating Average Traffic Speeds on IRN
Egress Engine
External Services (Data.gov.hk, TIS, TIMS)
ALPR Detectors
ALPR Software
Validated AID & BT data
Average Speeds on IRN Segments
Traffic data and average speeds on IRN
BT data
ALPR data
AID data
In the project, average speeds are estimated based on AID and BT data, while ALPR data are used for vehicle classification.

## Slide 41: End